## Slide 1
Zero defect manufacturing strategies for reduction of scrap and inspection effort in multi-stage production systems
F. Eger, D. Coupek, D. Caputo, M. Colledani et al.
Institute for Control Engineering of Machine Tools and Manufacturing Units (ISW), Seidenstraße 36, 70174 Stuttgart, Germany
Notes: Good … ladies and gentlemen, my name is F.E. I am a researcher at the Institute for Control Engineering at the U. of Stuttgart. It is my pleasure to present my research project ForZDM which deals with title….

## Slide 2
Content
Introduction
Problems
Solutions approaches
  Process data analysis
  Process control
  Monitoring
  Downstream compensation
Summary
Source: GKN Aerospace
Notes: After a brief introduction into the ZDM topic and stating (vorstellen) the problems that arise from this ZDM. I will be presenting the solution approaches. These approaches will focus on Process data analysis ….and downstream compensation.

## Slide 3
Production of rotating components
Component features:
Slim components () in cavity design
Turbine shaft in lightweight construction
 thin-walled product
Narrow zones of tolerance for geometric features
Focus on safety (high speeds)
  No air inclusions
  High surface quality
  No imbalances
L
D
d
Notes: The main focus lies on the production of rotating components which in this case can be found in turbine shafts aerospace and axles of railways. Like for any other product developing process it is subject to production efficiency (means more efficient processes), flexibility (easier adjustment to new requirements by the client), Quality (high safety standards) and time to market (speaks for itself).
The question is now why this is a problem? If we look at the features of these rotating components we see that these are slim components meaning there length is much larger than there diameter shown here in the picture. A special requirement is a lightweight construction which gives a thin walled product. This implies small tolerances on the geometric features. As mentioned earlier high safety standards especially for with high revolutions per minute have to be met (erfüllt werden) which means there should not be any air inclusions, the surface has to be of high quality and the part requires no imbalances. To understand how these requirements can be met we have to take a closer look at the production steps involved.

## Slide 4: Generalized production strategy of rotating components
Internal
contour
Finish
(painting)
External
references
Internal ref (bottle boring)
External
contour
EOL – Balancing process
Edge
cutting
Smelting in
furnace
Forging
Heat
treatment
Legend:
Process
Challenges:
Complexity of work steps (e. g. bottle boring – internal contour)
Number of work steps (approx. 30 processing steps – depending on the geometry)
Mainly end-of-line quality control
Inspection
Notes: Generally the production strategy involves 10 steps. Starting with smelting of the raw materials these are than forged and edges are cut off. Inner tension is reduced by a following heat treatment. The mechanical processes start with bottle boring which yields the first axis of reference. Based on this axis the external reference is made. Now the actual internal and external contours are made before finishing the part. One might think the product is ready for shipping now, however, due to the relative referencing of each subsequent step defect propagation reduces the product quality. This can only be compensated for with an EOL inspection (balancing process).
An EOL is performed … To further on the stand the magnitude (Ausmaß) of the defects (KLICK)

## Slide 5
Content
Introduction
Problems
Solutions approaches
  Process data analysis
  Process control
  Monitoring
  Downstream compensation
Summary
Notes: We will in depth look at the source of the defects…. (KLICK)

## Slide 6: Defect propagation in multi-stage production systems
Imbalance in workpieces:
Faulty processes can cause imbalances
Deviations accumulate over the entire process chain
Possible reasons for imbalances:
  Geometric deviations (e.g. imprecisions of the processing machines)
  Material inclusions (e.g. cavities, foreign material)
  Tensions (e.g. forging process, heat treatment)
P1
Pn+1
P2
P3
Pn
PB
Accumulation of deviations leads to imbalance
Rework / scrap
Process
Workpiece
Legend
Imbalance
No imbalance
60-90 man-hours (h)
15 h (14 - 20%)
Balancing process
Production process of the shaft
Notes: In order to explain the problem I will – leads to Imbalance in workpiece… become more and more … occure

## Slide 7: End-Of-Line (EOL) quality control
End-Of-Line (EOL) quality control:
Testing of the final product at the end of the process chain
Drawbacks:
Late detection of scrap (waste of resources)
Complicated diagnosis of defects
Machining of defective workpieces
  Waste of: money, energy, time, material, machine capacity
Objective:
Development of an alternative solution / supplements to EOL tests
Early defect diagnosis and correction

## Slide 8
Content
Introduction
Problems
Solutions approaches
  Process data analysis
  Process control
  Monitoring
  Downstream compensation
Summary

## Slide 9: ForZDM – Zero Defect Manufacturing
Objective:
Decrease the occurrence of defects and avoid defect propagation
Procedure:
Evaluation of existing and additional sensor systems – data analysis (Big Data)
Avoiding defect emergence (process control)
Preventing defect propagation
Used in production of rotating workpieces
MANUFACTURING INDUSTRY
Aerospace
Medicine
Railway
TECH. PROVIDERS & SYSTEMS INTEGRATORS
RESEARCH INSTITUTIONS
“This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 723698”
This presentation reflects only the authors’ views and the Commission is not responsable for any use that may be made of the information contained therein

## Slide 10: Hierarchical structure
Idea: Development of generic solutions for multi-stage production systems
P1
Pn+1
P2
P3
Pn
W1
W2
W2
W3
W3
Wn
W4
W3
W4
W1
W1
W1
W1
W2
W2
Evaluation of all workpieces and processes
In-line process control
Evaluation of all workpieces within a process
Evaluation of one workpiece throughout all processes
II.
IV.
III.
I.
Process
Workpiece
Legend

## Slide 11: I. Process data analysis – Big Data
Analysis of all measured variables
P1
Pn+1
P2
P3
Pn
W1
W2
W2
W3
W3
Wn
W4
W3
W4
W1
W1
W1
W1
W2
W2
Database
Neural networks
Correlation analysis
Examples of Evaluation:
Disadvantages:
  Handling of large datasets (complexity, real-time requirements)
  Plausibility of results
Advantage:
  Dependencies are uncovered (e.g. correlation analysis)

## Slide 12: Process data analysis – correlation matrix
P3
P4
Pn
Pn+1
P2
P1
Based on cross correlation
Standardized  [-1;1]

## Slide 13: II. Process control
Individual processes can be improved by a simultaneous interaction of “Measuring and Acting”
Wx
Wx
Wx
Wx
Wx
Wx
Wx
Wx
P1
Pn
P2
P3
…
Disadvantages:
  Online sensor signals required
  Not every process is controllable
Advantages:
  Deviations from the nominal value (set point) can be corrected immediately
  With optimal process control no defect propagation

## Slide 14: III. Monitoring
Process monitoring, process-dependent analysis
W2
W3
W4
Wn
Chart: ØA at position x = 231 mm
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
value | 125.41 | 125.42 | 125.43 | 125.42 | 125.43 | 125.43 | 125.46 | 125.52 | 125.51 | 125.45 | 125.454 | 125.458 | 125.462 | 125.466
max | 125.5 | 125.5 | 125.5 | 125.5 | 125.5 | 125.5 | 125.5 | 125.5 | 125.5 | 125.5 | 125.5 | 125.5 | 125.5 | 125.5
min | 125.4 | 125.4 | 125.4 | 125.4 | 125.4 | 125.4 | 125.4 | 125.4 | 125.4 | 125.4 | 125.4 | 125.4 | 125.4 | 125.4
P1
Pn
P2
P3
…
Wx
W1
Wx
Wx
Wx
Disadvantages:
  No correction of deviations of individual workpieces
Advantages:
  Visible trends (e.g. tool wear)
  Detection of scrap parts at an early stage

## Slide 15: IV. Downstream compensation (feed forward control)
Early detection and downstream correction of the imbalance
  Early detection of deviations based on machine data and sensor systems
  Identification of adequate corrective measures
 Imbalance measurement
 Correction of imbalance
Process
Workpiece
Legend
Imbalance
No Imbalance
P1
Pn
P2
P3
…
Disadvantages:
  Correlation required
Advantages:
  Avoiding rejects in the EOL test

## Slide 16: Measurement and correction strategies of imbalances
Objective: Correction of imbalance with existing facilities
Research needed:
Classification of imbalance cases
Derivation of compensation method (identification of downstream processes and intervention possibilities)
Classification
Data acquisition and analysis
Compensation method
Neural networks
Correlation analysis
Fuzzy logic
Balanced component
U1
Un
U2
…

## Slide 17
Content
Introduction
Problems
Solutions approaches
  Process data analysis
  Process control
  Monitoring
  Downstream compensation
Summary

## Slide 18: Summary
Objective: Development of an alternative/supplement to the widespread EOL tests
Expected results:
Reduction of production costs
Reduction of scrap parts
Increase of production flexibility and productivity
Adaption of subsequent processes
ForZDM
approach
Correction of errors
Minimization of defect emergence
In-line repair
Downstream

## Slide 19
Zero defect manufacturing strategies for reduction of scrap and inspection effort in multi-stage production systems
F. Egera, D. Coupeka, D. Caputob, M. Colledanic, M. Penalvad, J. A. Ortize, H. Freibergerf, G. Kolleggerg
aInstitute for Control Engineering of Machine Tools and Manufacturing Units, Seidenstr. 36, Stuttgart 70174, Germany bGKN Aerospace Engine Systems Norway, Kirkegårdsveien 45 N-3616 Kongsberg, Norway cPolitecnico di Milano, Department of Mechanical Engineering, Via la Masa, 1, 20156 Milan, Italy dTecnalia Research & Innovation, Mikeletegi 7, Donostia-San Sebastián 20009, Spain eIK4-Ideko, Arriaga Industrialdea 2, Elgoibar, 20870, Spain fABF Industrielle Automation GmbH, Deggendorfstraße 6, A-4030 Linz gnxtControl GmbH, Aumühlweg 3/B1, A-2544 Leobersdorf, Austria